## Slide 1
AVOIP MONITOR
NVX Preview
Dashboard
Monitor all your Crestron DM-NVX devices from one screen
Making Things Easier | AV-over-IP Monitoring Tool
Lucky Parihar
v1.0 Initial Release

## Slide 2
What is NVX Preview Dashboard?
A lightweight local monitoring tool for Crestron DM-NVX AV-over-IP devices.
ONE SCREEN
See live JPEG previews of all NVX
devices on a single dashboard.
ONLINE / OFFLINE
Instantly know which devices are
online or offline at a glance.
ANY NETWORK
Works over WiFi or wired.
Key Features
Auto-refresh every 10 seconds — configurable to 5s, 15s, 30s
Filter by location — Floor 1, Floor 2, Auditorium, Server Room
Search by device name or IP address
Click any device card to expand full-size preview
Credentials are protected — stops polling after 3 failed login attempts

## Slide 3
Who Is This Built For?
Project Engineers
Verify all NVX devices are live the moment commissioning starts
Service Engineers
Diagnose faults from your seat — not your feet
Resident Engineers
Monitor your entire AV infrastructure from one screen
Technicians
Level 1 troubleshooting in under 60 seconds
Commissioners
Validate signal flow across all endpoints before client handover
AV Professionals
Show clients a live system health view they will remember

## Slide 4
Installation — Step by Step
01
Install Python
Download from python.org/downloads
During install — tick Add Python to PATH
02
Install Packages
pip install fastapi uvicorn[standard] aiohttp
03
Add Your Devices
Edit devices.json with NVX IP addresses,
names, locations, and credentials
04
Run the Dashboard
python app.py
Browser opens at http://localhost:8000

## Slide 5
Configuring Your Devices — devices.json
Edit this file to add all your NVX devices. No Python knowledge required.
[
{
"id": "nvx-01",
"name": "Boardroom",
"ip": "10.1.20.14",
"location": "Floor 1",
"username": "admin",
"password": "Admin@123",
"preview_path": "/preview/preview_540px.jpeg",
"use_https": true
}
]
Field Reference
id
Unique ID per device (nvx-01, nvx-02...)
name
Display name on dashboard card
ip
IP address or hostname of NVX device
location
Groups devices into filter tabs
username
NVX web interface login username
password
NVX web interface login password
preview_path
Leave as default for all NVX devices
use_https
Set true — NVX uses HTTPS by default

## Slide 6
Resources
GitHub Repository
Source code, installation guide, devices.json template and full documentation.
Go-to-github
Watch — How to Use
Step-by-step video walkthrough covering setup, configuration, and live demo.
Video Link
Additional Resources
Architecture Overview
Full system architecture diagram showing all layers and data flow
devices.json Template
Ready-to-use template with all fields — just replace the IP addresses
Troubleshooting Guide
Step-by-step fixes for common issues — auth errors, offline devices

## Slide 7
Get Stuck? Need Support?
Contact me directly — I am happy to help you set this up on your project.
Name
Lucky Parihar
Email
Lucky.Parihar@avispl.com
LinkedIn
linkedin.com/in/lucky-parihar-b90425208
NVX Preview Dashboard | v1.0 | Lucky Parihar | 2026